## Slide 1: CE 530 Molecular Simulation
Lecture 20
Phase Equilibria
David A. Kofke
Department of Chemical Engineering
SUNY Buffalo
kofke@eng.buffalo.edu

## Slide 2: Thermodynamic Phase Equilibria
Certain thermodynamic states find that two (or more) phases may be equally stable
  thermodynamic phase coexistence
Phases are distinguished by an order parameter; e.g.
  density
  structural order parameter
  magnetic or electrostatic moment
Intensive-variable requirements of phase coexistence
  T = T
  P = P
  i = i, i = 1,…,C

## Slide 3: Phase Diagrams
Phase behavior is described via phase diagrams
Gibbs phase rule
  F = 2 + C – P
    F = number of degrees of freedom
      independently specified thermodynamic state variables
    C = number of components (chemical species) in the system
    P = number of phases
  Single component, F = 3 – P
Field variable
e.g., temperature
Density variable
L+V
tie line
V
L
S
S+V
L+S
triple point
critical point
Field variable
(pressure)
Field variable
(temperature)
V
L
S
critical point
isobar
two-phase regions
two-phase lines

## Slide 4: Approximate Methods for Phase Equilibria by Molecular Simulation 1.
Adjust field variables until crossing of phase transition is observed
  e.g., lower temperature until condensation/freezing occurs
Problem: metastability may obsure location of true transition
Try it out with the LJ NPT-MC applet
Pressure
Temperature
V
L
S
Metastable region
Temperature
Density
L
S
S+V
L+S
isobar
L+V
V
Hysteresis

## Slide 5: Approximate Methods for Phase Equilibria by Molecular Simulation 2.
Select density variable inside of two-phase region
  choose density between liquid and vapor values
Problem: finite system size leads to large surface-to-volume ratios for each phase
  bulk behavior not modeled
Metastability may still be a problem
Try it out with the SW NVT MD applet
Temperature
Density
L
S
S+V
L+S
L+V
V

## Slide 6: Rigorous Methods for Phase Equilibria by Molecular Simulation
Search for conditions that satisfy equilibrium criteria
  equality of temperature, pressure, chemical potentials
Difficulties
  evaluation of chemical potential often is not easy
  tedious search-and-evaluation process
Chemical potential
Simulation data
Simulation data or
equation of state
T constant
Pressure

## Slide 7: Rigorous Methods for Phase Equilibria by Molecular Simulation
Search for conditions that satisfy equilibrium criteria
  equality of temperature, pressure, chemical potentials
Difficulties
  evaluation of chemical potential often is not easy
  tedious search-and-evaluation process
Chemical potential
Simulation data or
equation of state
T constant
Pressure

## Slide 8: Rigorous Methods for Phase Equilibria by Molecular Simulation
Search for conditions that satisfy equilibrium criteria
  equality of temperature, pressure, chemical potentials
Difficulties
  evaluation of chemical potential often is not easy
  tedious search-and-evaluation process
Chemical potential
Simulation data or
equation of state
T constant
Pressure

## Slide 9: Rigorous Methods for Phase Equilibria by Molecular Simulation
Search for conditions that satisfy equilibrium criteria
  equality of temperature, pressure, chemical potentials
Difficulties
  evaluation of chemical potential often is not easy
  tedious search-and-evaluation process
Chemical potential
Simulation data or
equation of state
T constant
Pressure

## Slide 10: Rigorous Methods for Phase Equilibria by Molecular Simulation
Search for conditions that satisfy equilibrium criteria
  equality of temperature, pressure, chemical potentials
Difficulties
  evaluation of chemical potential often is not easy
  tedious search-and-evaluation process
Chemical potential
×
Simulation data or
equation of state
Coexistence
T constant
Pressure

## Slide 11: Rigorous Methods for Phase Equilibria by Molecular Simulation
Search for conditions that satisfy equilibrium criteria
  equality of temperature, pressure, chemical potentials
Difficulties
  evaluation of chemical potential often is not easy
  tedious search-and-evaluation process
Chemical potential
×
Simulation data or
equation of state
Coexistence
T constant
Pressure
Pressure
Temperature
V
L
S
+
Many simulations to get one point on phase diagram

## Slide 12: Gibbs Ensemble 1.
Panagiotopoulos in 1987 introduced a clever way to simulate coexisting phases without an interface
Thermodynamic contact without physical contact
  How?
Two simulation volumes

## Slide 13: Gibbs Ensemble 2.
MC simulation includes moves that couple the two simulation volumes
Try it out with the LJ GEMC applet
Particle exchange equilibrates chemical potential
Volume exchange equilibrates pressure
Incidentally, the coupled moves enforce mass and volume balance

## Slide 14: Gibbs Ensemble Formalism
Partition function
Limiting distribution
General algorithm. For each trial:
  with some pre-specified probability, select
    molecules displacement/rotation trial
    volume exchange trial
    molecule exchange trial
  conduct trial move and decide acceptance

## Slide 15: Molecule-Exchange Trial Move Analysis of Trial Probabilities
Detailed specification of trial moves and probabilities
Forward-step trial probability
Scaled volume
Reverse-step trial probability
χ is formulated to satisfy detailed balance

## Slide 16: Molecule-Exchange Trial Move Analysis of Detailed Balance
Detailed balance
πi
πij
πj
πji
=
Limiting distribution
Forward-step trial probability
Reverse-step trial probability

## Slide 17: Molecule-Exchange Trial Move Analysis of Detailed Balance
Detailed balance
πi
πij
πj
πji
=
Forward-step trial probability
Reverse-step trial probability
Limiting distribution

## Slide 18: Molecule-Exchange Trial Move Analysis of Detailed Balance
Detailed balance
πi
πij
πj
πji
=
Forward-step trial probability
Reverse-step trial probability
Acceptance probability

## Slide 19: Volume-Exchange Trial Move Analysis of Trial Probabilities
Take steps in λ = ln(VA/VB)
Detailed specification of trial moves and probabilities
Forward-step trial probability
Reverse-step trial probability

## Slide 20: Volume-Exchange Trial Move Analysis of Detailed Balance
Detailed balance
πi
πij
πj
πji
=
Limiting distribution
Forward-step trial probability
Reverse-step trial probability

## Slide 21: Volume-Exchange Trial Move Analysis of Detailed Balance
Detailed balance
πi
πij
πj
πji
=
Limiting distribution
Forward-step trial probability
Reverse-step trial probability

## Slide 22: Volume-Exchange Trial Move Analysis of Detailed Balance
Detailed balance
πi
πij
πj
πji
=
Forward-step trial probability
Reverse-step trial probability
Acceptance probability

## Slide 23: Gibbs Ensemble in the Molecular Simulation API

## Slide 24: Gibbs Ensemble MC Examination of Java Code. General
//Performs basic GEMC trial
//At present, suitable only for single-component systems
public void doStep() {
int i = (int)(rand.nextDouble()*iTotal); //select type of trial to perform
if(i < iDisplace) { //displace a randomly selected atom
if(rand.nextDouble() < 0.5) {atomDisplace.doTrial(firstPhase);}
else {atomDisplace.doTrial(secondPhase);}
}
else if(i < iVolume) { //volume exchange
trialVolume();
}
else { //molecule exchange
if(rand.nextDouble() < 0.5) {
trialExchange(firstPhase,secondPhase,firstPhase.parentSimulation.firstSpecies);
}
else {
trialExchange(secondPhase,firstPhase,firstPhase.parentSimulation.firstSpecies);
}
}
}
public class IntegratorGEMC extends Integrator

## Slide 25: Gibbs Ensemble MC Examination of Java Code. Molecule Exchange
/**
* Performs a GEMC molecule-exchange trial
*/
private void trialExchange(Phase iPhase, Phase dPhase, Species species) {
Species.Agent iSpecies = species.getAgent(iPhase); //insertion-phase speciesAgent
Species.Agent dSpecies = species.getAgent(dPhase); //deletion-phase species Agent
double uNew, uOld;
if(dSpecies.nMolecules == 0) {return;} //no molecules to delete; trial is over
Molecule m = dSpecies.randomMolecule(); //select random molecule to delete
uOld = dPhase.potentialEnergy.currentValue(m); //get its contribution to energy
m.displaceTo(iPhase.randomPosition()); //place at random in insertion phase
uNew = iPhase.potentialEnergy.insertionValue(m); //get its new energy
if(uNew == Double.MAX_VALUE) { //overlap; reject
m.replace(); //put it back
return;
}
double bFactor = dSpecies.nMolecules/dPhase.volume()//acceptance probability
* iPhase.volume()/(iSpecies.nMolecules+1)
* Math.exp(-(uNew-uOld)/temperature);
if(bFactor > 1.0 || bFactor > rand.nextDouble()) { //accept
iPhase.addMolecule(m,iSpecies); //place molecule in phase
}
else { //reject
m.replace(); //put it back
}
}
public class IntegratorGEMC extends Integrator

## Slide 26: Gibbs Ensemble MC Examination of Java Code. Volume Exchange
private void trialVolume() {
double v1Old = firstPhase.volume();
double v2Old = secondPhase.volume();
double hOld = firstPhase.potentialEnergy.currentValue() + secondPhase.potentialEnergy.currentValue();
double vStep = (2.*rand.nextDouble()-1.)*maxVStep; //uniform step in volume
double v1New = v1Old + vStep;
double v2New = v2Old - vStep;
double v1Scale = v1New/v1Old;
double v2Scale = v2New/v2Old;
double r1Scale = Math.pow(v1Scale,1.0/(double)Simulation.D);
double r2Scale = Math.pow(v2Scale,1.0/(double)Simulation.D);
firstPhase.inflate(r1Scale); //perturb volumes
secondPhase.inflate(r2Scale);
double hNew = firstPhase.potentialEnergy.currentValue() //acceptance probability + secondPhase.potentialEnergy.currentValue();
if(hNew >= Double.MAX_VALUE ||
Math.exp(-(hNew-hOld)/temperature
+ firstPhase.moleculeCount*Math.log(v1Scale)
+ secondPhase.moleculeCount*Math.log(v2Scale))
< rand.nextDouble())
{ //reject; restore volumes
firstPhase.inflate(1.0/r1Scale);
secondPhase.inflate(1.0/r2Scale);
}
//accept; nothing more to do
}
public class IntegratorGEMC extends Integrator

## Slide 27: Gibbs Ensemble Limitations
Limitations arise from particle-exchange requirement
  Molecular dynamics (polarizable models)
  Dense phases, or complex molecular models
  Solid phases
    N = 4n3 (fcc)
and sometimes from the volume-exchange requirement too
?

## Slide 28: Approaching the Critical Point
Critical phenomena are difficult to capture by molecular simulation
Density fluctuations are related to compressibility
Correlations between fluctuations important to behavior
  in thermodynamic limit correlations have infinite range
  in simulation correlations limited by system size
  surface tension vanishes
Pressure
Density
L+V
V
L
S
S+V
L+S
C
isotherm

## Slide 29: Critical Phenomena and the Gibbs Ensemble
Phase identities break down as critical point is approached
  Boxes swap “identities” (liquid vs. vapor)
  Both phases begin to appear in each box
    surface free energy goes to zero

## Slide 30: Gibbs-Duhem Integration
GD equation can be used to derive Clapeyron equation
  equation for coexistence line
Treat as a nonlinear first-order ODE
  use simulation to evaluate right-hand side
Trace an integration path the coincides with the coexistence line
Field variable
(pressure)
Field variable
(temperature)
V
L
S
critical point

## Slide 31: GDI Predictor-Corrector Implementation
lnp
β
lnp
lnp
β
β
Given initial condition and slope (= –Δh/ΔZ), predict new (p,T) pair.
Evaluate slope at new state condition…
…and use to correct estimate of new (p,T) pair

## Slide 32: GDI Simulation Algorithm
Estimate pressure and temperature from predictor
Begin simultaneous NpT simulation of both phases at the estimated conditions
As simulation progresses, estimate new slope from ongoing simulation data and use with corrector to adjust p and T
Continue simulation until the iterations and the simulation averages converge
Repeat for the next state point
Each simulation yields a coexistence point.
Particle insertions are never attempted.

## Slide 33: GDI Sources of Error
Three primary sources of error in GDI method
1
Stochastic error
lnp
β
2
Uncertainty in slopes due to uncertainty in simulation averages
Quantify via propagation of error using confidence limits of simulation averages
Finite step of integrator
Smaller step
Integrate series with every-other datum
Compare predictor and corrector values
Stability
Stability can be quantified
Error initial condition can be corrected even after series is complete
1
2
1
2
True curve
?
Incorrect initial condition

## Slide 34: GDI Applications and Extensions
Applied to a pressure-temperature phase equilibria in a wide variety of model systems
  emphasis on applications to solid-fluid coexistence
Can be extended to describe coexistence in other planes
  variation of potential parameters
    inverse-power softness
    stiffness of polymers
    range of attraction in square-well and triangle-well
    variation of electrostatic polarizability
  as with free energy methods, need to identify and measure variation of free energy with potential parameter
  mixtures

## Slide 35: Semigrand Ensemble
Thermodynamic formalism for mixtures
Rearrange
Legendre transform
  Independent variables include N and Δ2
  Dependent variables include N2
    must determine this by ensemble average
    ensemble includes elements differing in composition at same total N
Ensemble distribution

## Slide 36: GDI/GE with the Semigrand Ensemble
Governing differential equation (pressure-composition plane)
Simple LJ Binary

## Slide 37: GDI with the Semigrand Ensemble
Freezing of polydisperse hard spheres
  appropriate model for colloids
Integrate in pressure-polydispersity plane
Findings
  upper polydisersity bound to freezing
  re-entrant melting
solid
fluid
Composition
(Fugacity)
Diameter
m2
ν

## Slide 38: Other Views of Coexistence Surface
Dew and bubble lines
Residue curves
Azeotropes
  semigrand ensemble
  formulate appropriate differential equation
  integrate as in standard GDI method
    right-hand side involves partial molar properties

## Slide 39: Tracing of Azeotropes
Lennard-Jones binary, variation with intermolecular potential
  σ11 = 1.0; σ12 = 1.05; σ22 = variable
  ε11 = 1.0; ε12 = 0.90; ε22 = 1.0
  T = 1.10

## Slide 40: Summary
Thermodynamic phase behavior is interesting and useful
Obvious methods for evaluating phase behavior by simulation are too approximate
Rigorous thermodynamic method is tedious
Gibbs ensemble revolutionized methodology
  two coexisting phases without an interface
Gibbs-Duhem integration provides an alternative to use in situations where GE fails
  dense and complex fluids
  solids
Semigrand ensemble is useful formalism for mixtures
GDI can be extended in many ways