## Slide 1: CE 530 Molecular Simulation
Lecture 18
Free-energy calculations
David A. Kofke
Department of Chemical Engineering
SUNY Buffalo
kofke@eng.buffalo.edu

## Slide 2: Free-Energy Calculations
Uses of free energy
  Phase equilibria
  Reaction equilibria
  Solvation
  Stability
  Kinetics
Calculation methods
  Free-energy perturbation
  Thermodynamic integration
  Parameter-hopping
  Histogram interpolation

## Slide 3: Ensemble Averages
Simple ensemble averages are of the form
To evaluate:
  sample points in phase space with probability π(Γ)
  at each point, evaluate M(Γ)
  simple average of all values gives <M>
Previous example
  mean square distance from origin in region R
  sample only points in R, average r2
Principle applies to both MD and MC
Γ

## Slide 4: Ensemble Volumes
Entropy and free energy relate to the size of the ensemble
  e.g., S = k lnΩ(E,V,N)
No effective way to measure the size of the ensemble
  no phase-space function that gives size of R while sampling only R
    imagine being place repeatedly at random points on an island
    what could you measure at each point to determine the size of the island?
Volume of ensemble is numerically unwieldy
  e.g. for 100 hard spheres
     = 0.1, Ω = 5 × 10133
     = 0.5, Ω = 3 × 107
     = 0.9, Ω = 5 × 10-142
Shape of important region is very complex
  cannot apply methods that exploit some simple geometric picture
Ω = number of states of given E,V,N
Γ

## Slide 5: Reference Systems
All free-energy methods are based on calculation of free-energy differences
Example
  volume of R can be measured as a fraction of the total volume
    sample the reference system
    keep an average of the fraction of time occupying target system
  what we get is the difference
Usefulness of free-energy difference
  it may be the quantity of interest anyway
  if reference is simple, its absolute free energy can be evaluated analytically
    e.g., ideal gas, harmonic crystal
Γ

## Slide 6: Hard Sphere Chemical Potential
Chemical potential is an entropy difference
For hard spheres, the energy is zero or infinity
  any change in N that does not cause overlap will be change at constant U
To get entropy difference
  simulate a system of N+1 spheres, one non-interacting “ghost”
  occasionally see if the ghost sphere overlaps another
  record the fraction of the time it does not overlap
Here is an applet demonstrating this calculation
N+1
N

## Slide 7: Free-Energy Perturbation
Widom method is an example of a free-energy perturbation (FEP) technique
FEP gives free-energy difference between two systems
  labeled 0, 1
Working equation
Γ
0
1
Free-energy difference is a ratio of partition functions

## Slide 8: Free-Energy Perturbation
Widom method is an example of a free-energy perturbation (FEP) technique
FEP gives free-energy difference between two systems
  labeled 0, 1
Working equation
Γ
0
1
Add and subtract reference-system energy

## Slide 9: Free-Energy Perturbation
Widom method is an example of a free-energy perturbation (FEP) technique
FEP gives free-energy difference between two systems
  labeled 0, 1
Working equation
Γ
0
1
Identify reference-system probability distribution

## Slide 10: Free-Energy Perturbation
Widom method is an example of a free-energy perturbation (FEP) technique
FEP gives free-energy difference between two systems
  labeled 0, 1
Working equation
Sample the region important to 0 system, measure properties of 1 system
Γ
0
1
Write as reference-system ensemble average

## Slide 11: Chemical potential
For chemical potential, U1 - U0 is the energy of turning on the ghost particle
  call this ut, the “test-particle” energy
  test-particle position may be selected at random in simulation volume
  for hard spheres, e-βut is 0 for overlap, 1 otherwise
    then (as before) average is the fraction of configurations with no overlap
This is known as Widom’s insertion method

## Slide 12: Widom’s Method. Java Code
public class MeterWidomInsertion extends Meter
/**
* Performs insertion average used in chemical-potential calculation
*/
public double currentValue() {
double sum = 0.0; //zero sum for insertion average
phase.addMolecule(molecule,speciesAgent); //place molecule in phase
for(int i=nInsert; i>0; i--) { //perform nInsert insertions
molecule.translateTo(phase.randomPosition()); //select random position
double u = phase.potentialEnergy.currentValue(molecule); //compute energy
if(u < Double.MAX_VALUE) //add to test-particle average
sum += Math.exp(-u/(phase.integrator().temperature()));
}
phase.deleteMolecule(molecule); //remove molecule from phase
if(!residual) sum *= speciesAgent.moleculeCount/phase.volume(); //multiply by Ni/V
return sum/(double)nInsert; //return average
}
//Method to identify species for chemical-potential calculation by this meter
//Normally called only once in a simulation
public void setSpecies(Species s) {
species = s;
molecule = species.getMolecule();
if(phase != null) speciesAgent = species.getAgent(phase);
}

## Slide 13: Deletion Method
The FEP formula may be used also with the roles of the reference and target system reversed
  sample the 1 system, evaluate properties of 0 system
Consider application to hard spheres
  eβut is infinity for overlap, 0 otherwise
  but overlaps are never sampled
  true average is product of 0 × ∞
    technically, formula is correct
  in practice simulation average is always zero
    method is flawed in application
    many times the flaw with deletion is not as obvious as this
Γ
0
1
Original: 0  1
Modified: 1  0

## Slide 14: Other Types of Perturbation
Many types of free-energy differences can be computed
Thermodynamic state
  temperature, density, mixture composition
Hamiltonian
  for a single molecule or for entire system
  e.g., evaluate free energy difference for hard spheres with and without electrostatic dipole moment
Configuration
  distance/orientation between two solutes
  e.g, protein and ligand
Order parameter identifying phases
  order parameter is a quantity that can be used to identify the thermodynamic phase a system is in
  e.g, crystal structure, orientational order, magnetization

## Slide 15: General Numerical Problems
Sampling problems limit range of FEP calculations
Target system configurations must be encountered when sampling reference system
Two types of problem arise
  first situation is more common
    although deletion FEP provides an avoidable example of the latter
Γ
0
1
target-system space very small
Γ
0
1
target system outside of reference

## Slide 16: Staging Methods
Multistage FEP can be used to remedy the sampling problem
  define a potential Uw intermediate between 0 and 1 systems
  evaluate total free-energy difference as
Each stage may be sampled in either direction
  yielding four staging schemes
  choose to avoid deletion calculation
Γ
0
1
W
Use staged insertion
Use umbrella sampling
Γ
0
1
W
Γ
0
1
Use Bennett’s method
W

## Slide 17: Example of Staging Method
Hard-sphere chemical potential
Use small-diameter sphere as intermediate
In first stage, measure fraction of time random insertion of small sphere finds no overlap
In second stage, small sphere moves around with others. Measure fraction of time no overlap is found when it is grown to full-size sphere
Γ

## Slide 18: Multiple Stages
Γ
0
1
W1
W2
W3
Γ
0
1
W1
W2
W3
Γ
0
1
W1
W3
W2
Multistage insertion
Multistage umbrella sampling
Multistage Bennett’s method

## Slide 19: Non-Boltzmann Sampling
The FEP methods are an instance of a more general technique that aims to improve sampling
Unlike biasing methods, improvement entails a change in the limiting distribution
Apply a formula to recover the correct average
Γ
W
0
0

## Slide 20: Thermodynamic Integration 1.
Thermodynamics gives formulas for variation of free energy with state
These can be integrated to obtain a free-energy difference
  derivatives can be measured as normal ensemble averages
  this is usually how free energies are “measured” experimentally

## Slide 21: Thermodynamic Integration 2.
TI can be extended to follow uncommon (or unphysical) integration paths
  much like FEP, can be applied for any type of free-energy change
Formalism
  Let λ be a parameter describing the path
  the potential energy is a function of λ
  ensemble formula for the derivative
  then

## Slide 22: Thermodynamic Integration Example
The soft-sphere pair potential is given by
Softness and range varies with n
  large n limit leads to hard spheres
  small n leads to Coulombic behavior
Thermodynamic integration can be used to measure free energy as a function of softness s = 1/n
  Integrand is
Exhibits simplifying behavior because εσn is the only potential parameter

## Slide 23: Parameter Hopping. Theory
View free-energy parameter λ as another dimension in phase space
Partition function
Monte Carlo trials include changes in λ
Probability that system has λ λ0 or λ = λ1
Γ

## Slide 24: Parameter Hopping. Implementation
Monte Carlo simulation in which -change trials are attempted
Accept trials as usual, with probability min[1,e-βΔU]
Record fractions f0, f1 of configurations spent in λ λ0 and λ = λ1
Free energy is given by ratio
In practice, system may spend almost no time in one of the values
  Can apply weighting function w(λ) to encourage it to sample both
  Accept trials with probability min[1,(wn/wo) e-βΔU]
  Free energy is
  Good choice for w has f1 = f0
Multivalue extension is particularly effective
   takes on a continuum of values

## Slide 25: Summary
Free energy calculations are needed to model the most interesting physical behaviors
  All useful methods are based on computing free-energy difference
Four general approaches
  Free-energy perturbation
  Thermodynamic integration
  Parameter hopping
  Distribution-function methods
FEP is asymmetric
  Deletion method is awful
Four approaches to basic multistaging
  Umbrella sampling, Bennett’s method, staged insertion/deletion
Non-Boltzmann methods improve sampling